## Slide 1: Design and Validation of a Constant Wall Temperature Plate
Drummond Biles Advisor: Chris White
University of New Hampshire
APS-DFD
24 November 2014
Special Thanks to:
Michael Allard, Allen Ma, and Reza Ebadi
THIS WORK IS SUPPORTED BY AN NSF/DOE PARTNERSHIP
AWARD’S: 1258702, 1258594, 1258697

## Slide 2
Non-Equilibrium Thermal Boundary Layers
Non-Equilibrium Boundary Layers brought about from;
.,. Pressure gradients
.,. Separation
.,. Dynamic walls
.,. Unsteady flow
In many engineering applications one or several of these effects are important
Equilibrium Boundary Layer
VACC, UVM

## Slide 3: CFD Wall models (Equilibrium Flows)
.,. Computationally expensive to solve near wall dynamics
.,. Near wall dynamics extrapolated from log profile
.,. Reasonable estimate for equilibrium wall flows
.,. Fail when applied
non-equilibrium boundary layers
Bradshaw et al., The law of the wall in turbulent flow

## Slide 4
Experimental Approach
Systematic and Simple
Design Constraints
Facility
.,. Length=2.75m
.,. Turbulent Management section (screens/honeycomb)
.,. Velocity 0.25 to 12m/sec (frequency controlled motor)
.,. Control Boundary Conditions
-Control T
∞
-Control To /heat flux
.,. Maintain attached boundary Layer
UNH Thermal Boundary Layer Wind Tunnel

## Slide 5
Prototype Sectioned Constant Wall Temperature Plate
.,. Size=0.45m x 0.65m
.,. Sectioned design∗
.,. Independently heated/controlled∗
.,. Individually Insulated
Front Convective Plate
* Blackwell, B. F., The turbulent boundary layer on a porous plate

## Slide 6: Temperature Controller
.,. Maintain temperature within + − 0.1o C
.,. Independently monitor and control each plate
Designed/Created by:Ebadi, Reza

## Slide 7: Spatial Temperature Distribution
7/14

## Slide 8: Spatial Temperature Distribution
Thermocouple #1 = 50o C Thermocouple #2 = 50.01o C
7/14

## Slide 9: Spatial Temperature Distribution
−30
−20
−10 0 10
Spanwise Distance (mm)
Spanwise Profile (camera reversed)
20
30
0.99
1
1.01
1.02
T/Tset
Spanwise Profile
#1
#2
#3
#4
#5
−30
−20
−10
0 10
20
30
1
0.99
1.01
Spanwise Distance (mm)
T/Tset
#1
#2
#3
#4
#5

## Slide 10: Temperature Profile
.,. Type K thermocouple
.,. Probe−diameter
δT
= 0.0212
.,. Downstream position=0.3 m
.,. Re = 5.7 ∗ 104
.,. Wall temperature= 60o C
.,. 30 points logarithmicly spaced
.,. Sampled at 2 Hz for 2 min
9/14

## Slide 11: Temperature Profile
10
−1
10
0
0
0.2
0.4
0.6
0.8
1
Temperature Profile Comparison
ηT
θ
Analytical
Experimental Confidence Interval
Non-dimensional variables∗∗:
.,. θ = T −T∞
Twall −T∞
.,. ηT = y
δT
.,. θA = 1 − 1.5η + .5η3
** Faghri, Amir, Advanced Heat and Mass Transfer
9/14

## Slide 12: Spanwise Variability
0
0.005
0.01 0.015
Height (m)
0.02
0.025
20
30
40
50
Temperature (c)
Temperature Profile
−2A
−A 0 A 2A
10/14

## Slide 13: Spanwise Variability
0
0.005
0.01 0.015
Height (m)
0.02
0.025
20
30
40
50
Temperature (c)
Temperature Profile
−2A
−A 0 A 2A
10−2
10−1
ηT
100
0
0.2
0.4
0.6
0.8
1
Normalized Temperature Profile
θ
−2A
−A
0
A
2A
+−2STD
10/14

## Slide 14
Single Perturbation
.,. 3cm Diameter
.,. Insulated
.,. D
δ = 10
11/14

## Slide 15: Single Perturbation
Set Temperature=30o C
Re = 9.4 ∗ 104
−50 0 50
Re = 1.88 ∗ 105
0
50
100
T/Tset
0.98
1
1.02
Re = 1.25 ∗ 105
−50 0 50
Re = 2.42 ∗ 105
0
50
100
T/Tset
0.98
1
1.02
Streamwise Distance (mm)
0
50
100
T/Tset
0.98
1
1.02
Streamwise Distance (mm)
0
50
100
T/T
set
0.98
1
1.02
−50
0
50
−50
0
50
Spanwise Distance (mm)
Spanwise Distance (mm)
11/14

## Slide 16: Single Perturbation
Set Temperature=60o C
Re = 9.4 ∗ 104
−50 0 50
Re = 1.88 ∗ 105
0
20
40
60
80
100
T/Tset
0.95
1
1.05
Re = 1.25 ∗ 105
−50 0 50
Re = 2.42 ∗ 105
0
20
40
60
80
100
T/Tset
0.95
1
1.05
Streamwise Distance (mm)
0
50
100
T/Tset
0.95
1
1.05
Streamwise Distance (mm)
0
20
40
60
80
100
T/T
set
0.95
1
1.05
−50
0
50
−50
0
50
Spanwise Distance (mm)
Spanwise Distance (mm)
11/14

## Slide 17: Final Wall Plate Design

## Slide 18
Conclusions
.,. Control set temperature to +-.1o C
.,. In equilibrium flow produce spatially uniform temperature to +-2%
.,. Produce 2D equilibrium thermal boundary layer
.,. Develop spatial structure resulting from non-uniform heat flux
Future Work
.,. Construct/Validate final plate design
.,. Investigate disturbance due to pressure gradient
.,. Investigate flow over 3D obstacle
.,. Investigate rapid periodic forcing on mean flow
.,. Investigate disturbance due to multiple perturbations on mean flow

## Slide 19: Questions??
VACC, UVM